## Slide 1
DIY
Switch Machine
DCC Decoder
Part 3

## Slide 2: Arduino Nano Accessory Decoder
Arduino Nano
DCC Track
5V
Connect up to 16 Servos SG90
3.5 - 8.4 Volts
DCC Interface
Buck Converter
Set to 7.5V
Connect up to 8 Tortoises or Double Magnet Drives
I2C GPIO Expander
PWM Driver

## Slide 3: Servo Decoder Requirements
Connects to DCC, no additional power supply
Individual Address for each Servo
Support of full Switch and Signal Address Ranges
Adjustable Rotation Angles per Servo
Adjustable Rotation Speed per Servo






## Slide 4: Servo Decoder Requirements Page 2
Supports Slow Motion Switch Machines
Supports 3 wire Solenoid Switch Machines
Supports 2 wire Solenoid Switch Machines
×
×
×

## Slide 5: Development Steps
Analyze new requirements
Develop a concept for the hardware
Develop a concept for the software
Implement Hardware and test
Implement Software and test
Debug, improve and finalize

## Slide 6: Table of Contents
Requirements Analysis: Controlling Switch machines
Building the hardware: Add 8 channels for Switch Machines
Testing the hardware
Software Development 1: Preparation
Software Development 2: Adding switch machine support
Conclusions
0:58
3:04
9:12
15:07
31:52
1:05:03

## Slide 7: Switch Machines
Type Example How to Control
Stall Motor Circuitron Tortoise
Limit Switch Motor Aristo 11299
3 Wire Solenoid Atlas Snap Switch
2 Wire Solenoid Kato N Scale
Additional information: https://dccwiki.com/Turnout_Motors
M
+
-
+
-
M
+
-
+
-
-
-
+
+
-
+
-
Polarity change
Permanent on
Polarity change
Permanent on
1 of 2 coils activated
Momentary on
Polarity change
Momentary on

## Slide 8: Hardware Design
Use Relay board with 2 relays per turnout, a total of 16 relays for 8 turnouts
  Alternatively we could use H-Bridges
Use MCP23017 GPIO Port Extender to control 16 IO’s via I2C Bus

## Slide 9: Software Requirements and Design
Support for Switch commands only (2 positions: CL / TH), no Signal commands (32 Aspects)
Programmable Duration of Activation
2 Step approach with Target and Timer as before
Individual Address and IO Ports
Plus: Individual Servo Speed for each direction

## Slide 10: Arduino Nano Accessory Decoder
Arduino Nano
DCC Track
5V
Connect up to 16 Servos SG90
3.5 - 8.4 Volts
DCC Interface
Buck Converter
Set to 7.5V
Connect up to 8 Tortoises or Double Magnet Drives
I2C GPIO Expander
PWM Driver

## Slide 11: Testing the Hardware
Install the Library Adafruit_MCP23017
Use and Improve the Toggle Example

## Slide 12: Building the Bridge
Third Improvement: Preparation
  Individual Rotation Speed in each direction
  Configurable Port Address
  Preparation for adding Relay Board
    Adding a driveType Configuration Variable
    Adding a Structure for type specific processing

## Slide 13: Building the Bridge
Fourth Improvement: Adding Relay Support
  Blocking out Signal Commands
  Differences between Relay and Servo Control
    On/off vs. continuous position command
    Relays can be retriggered
  Implementing Relay Control
  Testing and Performance Review

## Slide 14: Servo Decoder Requirements Page 2
Supports Slow Motion Switch Machines
Supports 3 wire Solenoid Switch Machines
Supports 2 wire Solenoid Switch Machines




## Slide 15
Additional Materials on Github: https://github.com/tanner87661/IoTT-Video19
Arduino Basics 101: https://www.youtube.com/watch?v=BtLwoNJ6klE
Arduino Basics 102: https://www.youtube.com/watch?v=YT3birSKLLU&t=398s
Arduino Basics 103: https://www.youtube.com/watch?v=EVm0qVJ56II
Arduino State Management: https://www.youtube.com/watch?v=3VZgaJBrZD8
Layout Intro Sequence Outdoor Layout: Beat Deola, Switzerland​
DCC Interface: If interested, send me a PM. I have some of the prototypes available for cost plus shipping.
Buck converter: https://www.amazon.com/MCIGICM-step-down-Converter-3-0-40V-1-5-35V/dp/B06XZ1DKF2/ref=sr_1_5?keywords=buck+converter&qid=1554521368&s=gateway&sr=8-5
Arduino Nano: https://www.amazon.com/gp/product/B01N7I0W77/ref=ppx_yo_dt_b_asin_image_o00_s00?ie=UTF8&psc=1
PWM driver: https://www.amazon.com/Onyehn-Channel-PCA9685-Arduino-Raspberry/dp/B07GJCPWW2/ref=pd_day0_hl_147_2/144-9269444-7135168?_encoding=UTF8&pd_rd_i=B07GJCPWW2&pd_rd_r=7c0128c8-581c-11e9-8362-b1c2d0dccc11&pd_rd_w=ebl7B&pd_rd_wg=XDjih&pf_rd_p=ad07871c-e646-4161-82c7-5ed0d4c85b07&pf_rd_r=MFZXEC12T0FFV415AHQ4&psc=1&refRID=MFZXEC12T0FFV415AHQ4
Micro Servos: https://www.amazon.com/Micro-Helicopter-Airplane-Remote-Control/dp/B072V529YD/ref=pd_bxgy_60_img_2/144-9269444-7135168?_encoding=UTF8&pd_rd_i=B072V529YD&pd_rd_r=86eda38f-581c-11e9-9502-091092cc734e&pd_rd_w=OfHyY&pd_rd_wg=VPeRR&pf_rd_p=a2006322-0bc0-4db9-a08e-d168c18ce6f0&pf_rd_r=PTY6VGCE68SEB9VVHH2E&psc=1&refRID=PTY6VGCE68SEB9VVHH2E
16 Channel Relay Board: https://www.amazon.com/gp/product/B0057OC66U/ref=ppx_yo_dt_b_asin_title_o01_s00?ie=UTF8&psc=1
16 bit GPIO Expander: https://www.amazon.com/gp/product/B07GRQWQF9/ref=ppx_yo_dt_b_asin_title_o01_s00?ie=UTF8&psc=1
Turnout Motors: https://dccwiki.com/Turnout_Motors